## Slide 1: Chapter 1
Preliminaries

## Slide 2: Language Evaluation Criteria
What things should we look at when deciding how “good” a language is?

## Slide 3: Language Evaluation Criteria
Readability: the ease with which programs can be read and understood
Writability: the ease with which a language can be used to create programs
Reliability: how well then language helps programmer avoid failures
  (or at least avoids “silent” failures)
Cost: the ultimate total cost

## Slide 4: Evaluation Criteria: Readability
What makes a language “Readable”?
Overall simplicity
  A manageable set of features and constructs
  Minimal feature multiplicity
    (Do we need count = count + 1 , count +=1 , and count++, and ++count?
  Sensible operator overloading
    Should “+” be both addition and string concatenation?
Orthogonality
  A relatively small set of primitive constructs can be combined in a relatively small number of ways
  Every possible combination is legal
    In other words, few exceptions (like void can be a return type but not a variable)
Data types
  Adequate predefined data types
Syntax considerations
  Form and meaning: self-descriptive constructs, meaningful keywords
    What does “static” mean in C? Is this term used consistently?
    Does the “*” operator have a consistent meaning in C?
    What does “grep” mean in the UNIX environment? Can you figure this out based on general computing knowledge?

## Slide 5: Evaluation Criteria: Readability
Should keywords be reserved words?
  In other words, is it reasonable to allow “for” “while”, etc. to be variable names?
Should blocks use braces, or words:
for (int j = 0; j < array.length; ++j) {
sum = sum + array[j];
}
for (int j = 0; j < array.length; ++j)
sum = sum + array[j];
end
for (int j = 0; j < array.length; ++j)
begin
sum = sum + array[j];
end

## Slide 6: Evaluation Criteria: Writability
Expressivity
  A set of relatively convenient ways of specifying operations
    “simple things should be simple. Complex things should not be impossible”
  Strength and number of operators and predefined functions
  “Right tools for the job”
Simplicity and orthogonality
  Few constructs, a small number of primitives, a small set of rules for combining them
  Why is this important? Why not have many options and just ignore the ones you don’t want/need?
Support for abstraction
  The ability to define and use complex structures or operations in ways that allow details to be ignored
  Avoid unnecessary repetition (DRY)

## Slide 7: Evaluation Criteria: Reliability
Reliability:
  Language should help you avoid errors
  If you make an error, it should be immediately obvious
Type checking
  Testing for type errors
Exception handling
  Intercept run-time errors and take corrective measures
Aliasing
  Presence of two or more distinct referencing methods for the same memory location
Readability and writability
  A language that does not support “natural” ways of expressing an algorithm will require the use of “unnatural” approaches, and hence reduced reliability

## Slide 8: Evaluation Criteria: Cost
Training programmers to use the language
Writing programs
  (depends on the domain --- “right tool for job”)
Executing programs
  Performance
Reliability: poor reliability leads to high costs
Maintaining programs
  Readability is a big factor here

## Slide 9: Evaluation Criteria: Others
Portability
  The ease with which programs can be moved from one implementation to another
Generality
  The applicability to a wide range of applications
Well-definedness
  The completeness and precision of the language’s official definition

## Slide 10: Tradeoffs
How does improving one area affect others?
Readability vs. Writability
use v5.10;
while (<STDIN>) {
chomp;
say if (/z/)
}
use v5.10;
while ($_ = <STDIN>)
{
chomp $_;
if ($_ =~ /MATCH/) {
say $_;
}
}

## Slide 11: Tradeoffs
Writability vs. Performance?
Writability vs. Reliability?
Reliability vs. Performance?

## Slide 12: Language Design Trade-Offs
Reliability vs. cost of execution
  Example: Java demands all references to array elements be checked for proper indexing, which leads to increased execution costs
Readability vs. writability
  Example: APL provides many powerful operators (and a large number of new symbols), allowing complex computations to be written in a compact program but at the cost of poor readability
Writability (flexibility) vs. reliability
  Example: C++ pointers are powerful and very flexible but are unreliable

## Slide 13: Origins of Modern Programming Languages
First electronic computers of the 1940s used machine language
  Sequence of 1s and 0s that correspond directly to wires in the CPU.
Register File
a1
a2
a3
rd1
rd2
wd
32
32
32
5
5
5
32
clock
Register 0
Register 1
Register 2
Register 31
…
000000000100001100001000000000
ALU Op Code
a1 and a2
a1 and a2
a1 a2 a3
unused
add r1 ← r2, r3

## Slide 14: Assembly the obvious next step
op code | rs | rt | rd | <unused>
000000 | 00010 | 00011 | 00001 | 000000000
6
add r1 ← r2, r3
5
5
5
9
= 32
Use words/numbers to represent each section of 1s and 0s
Originally each assembly instruction corresponded to exactly one machine instruction
Parameters are registers
More short-cuts (labels, macros) added later

## Slide 15: Next steps: Fortran, C, etc.
Each line of code corresponds to multiple machine instructions.
Use variables instead of registers
  Compiler keeps track of which variables are currently in which register.
Much easier to read and write
Compiler can do helpful error checking
  e.g., raise error if you try to treat a float as an int.
  This increases reliability
These language are called imperative languages
  They tell the CPU specifically what to do (like an imperative sentence)
Require programmers to “think like the CPU”
  Must rephrase the problem in your head to align with the way the CPU solves problems.
x = a + b + c

## Slide 16: Compilation
Translate high-level program (source language) into machine code (machine language)
Slow translation, fast execution
  Everything is “ready to go” when the program starts
  Each processor/OS combination needs its own binary
Compilation process has several phases:
  lexical analysis: converts characters in the source program into lexical units
  syntax analysis: transforms lexical units into parse trees which represent the syntactic structure of program
  Semantics analysis: generate intermediate code
    In C, this is assembly
  code generation: machine code is generated

## Slide 17: The Compilation Process

## Slide 18: Pure Interpretation
Think of a UNIX shell (e.g., bash)
  It is a programming language.
  Runs sequence of commands
  Has variables, if, loops, functions, etc.
This code usually can’t be compiled beforehand because you are “writing” the code one line at a time.
This type of programming language is “interpreted”
  Lines of code are processed and executed one a time.
Needs an executable called an Interpreter
  E.g, /bin/bash

## Slide 19: Pure Interpretation Process

## Slide 20: Pure Interpretation
Examples: Python, Ruby, PHP, JavaScript.
Cons:
  10 to 100 times slower than compiled programs
  Often uses more RAM
Pros:
  Source code is often more portable
    Interpreter must be ported, but source code should run on (almost) any machine with an interpreter
    Simplifies distribution because user need not recompile for his specific processor/OS combination.
  Interpreted languages are often more writable.
    In order to improve performance, compiled languages tend to be very “picky”.
    Interpreted languages are already slow, so they aren’t as “picky”

## Slide 21: Hybrid Implementation Systems
A compromise between compilers and pure interpreters
A high-level language program is translated to an intermediate language that allows easy interpretation
Faster than pure interpretation
Examples
  Perl programs are partially compiled to detect errors before interpretation
  Initial implementations of Java were hybrid; the intermediate form, byte code, provides portability to any machine that has a byte code interpreter and a run-time system (together, these are called Java Virtual Machine)

## Slide 22: Hybrid Implementation Process

## Slide 26: Instruction
Register File
a1
a2
a3
rd1
rd2
wd
32
32
32
5
5
5
32
clock
Register 0
Register 1
Register 2
Register 31
…
000000000100001100001000000000
ALU Op Code
a1 and a2
a1 and a2
a1 a2 a3
unused
add r1 ← r2, r3

## Slide 27: Influences on Language Design
Computer Architecture
  Languages are developed around the prevalent computer architecture, known as the von Neumann architecture
Program Design Methodologies
  New software development methodologies (e.g., object-oriented software development) led to new programming paradigms and by extension, new programming languages

## Slide 28: Computer Architecture Influence
Well-known computer architecture: Von Neumann
Imperative languages, most dominant, because of von Neumann computers
  Data and programs stored in memory
  Memory is separate from CPU
  Instructions and data are piped from memory to CPU
  Basis for imperative languages
    Variables model memory cells
    Assignment statements model piping
    Iteration is efficient

## Slide 29: The von Neumann Architecture

## Slide 30: The von Neumann Architecture
Fetch-execute-cycle (on a von Neumann architecture computer)
  initialize the program counter
  repeat forever
  fetch the instruction pointed by the counter
  increment the counter
  decode the instruction
  execute the instruction
  end repeat

## Slide 31: Programming Methodologies Influences
1950s and early 1960s: Simple applications; worry about machine efficiency
Late 1960s: People efficiency became important; readability, better control structures
  structured programming
  top-down design and step-wise refinement
Late 1970s: Process-oriented to data-oriented
  data abstraction
Middle 1980s: Object-oriented programming
  Data abstraction + inheritance + polymorphism

## Slide 32: Language Categories
Imperative
  Central features are variables, assignment statements, and iteration
  Include languages that support object-oriented programming
  Include scripting languages
  Include the visual languages
  Examples: C, Java, Perl, JavaScript, Visual BASIC .NET, C++
Functional
  Main means of making computations is by applying functions to given parameters
  Examples: LISP, Scheme, ML, F#
Logic
  Rule-based (rules are specified in no particular order)
  Example: Prolog
Markup/programming hybrid
  Markup languages extended to support some programming
  Examples: JSTL, XSLT

## Slide 33: Implementation Methods
Compilation
  Programs are translated into machine language; includes JIT systems
  Use: Large commercial applications
Pure Interpretation
  Programs are interpreted by another program known as an interpreter
  Use: Small programs or when efficiency is not an issue
Hybrid Implementation Systems
  A compromise between compilers and pure interpreters
  Use: Small and medium systems when efficiency is not the first concern

## Slide 34: Layered View of Computer
The operating system and language implementation are layered over
machine interface of a computer

## Slide 35: Compilation
Translate high-level program (source language) into machine code (machine language)
Slow translation, fast execution
Compilation process has several phases:
  lexical analysis: converts characters in the source program into lexical units
  syntax analysis: transforms lexical units into parse trees which represent the syntactic structure of program
  Semantics analysis: generate intermediate code
  code generation: machine code is generated

## Slide 36: The Compilation Process

## Slide 37: Additional Compilation Terminologies
Load module (executable image): the user and system code together
Linking and loading: the process of collecting system program units and linking them to a user program

## Slide 38: Von Neumann Bottleneck
Connection speed between a computer’s memory and its processor determines the speed of a computer
Program instructions often can be executed much faster than the speed of the connection; the connection speed thus results in a bottleneck
Known as the von Neumann bottleneck; it is the primary limiting factor in the speed of computers

## Slide 39: Pure Interpretation
No translation
Easier implementation of programs (run-time errors can easily and immediately be displayed)
Slower execution (10 to 100 times slower than compiled programs)
Often requires more space
Now rare for traditional high-level languages
Significant comeback with some Web scripting languages (e.g., JavaScript, PHP)

## Slide 40: Pure Interpretation Process

## Slide 41: Hybrid Implementation Systems
A compromise between compilers and pure interpreters
A high-level language program is translated to an intermediate language that allows easy interpretation
Faster than pure interpretation
Examples
  Perl programs are partially compiled to detect errors before interpretation
  Initial implementations of Java were hybrid; the intermediate form, byte code, provides portability to any machine that has a byte code interpreter and a run-time system (together, these are called Java Virtual Machine)

## Slide 42: Hybrid Implementation Process

## Slide 43: Just-in-Time Implementation Systems
Initially translate programs to an intermediate language
Then compile the intermediate language of the subprograms into machine code when they are called
Machine code version is kept for subsequent calls
JIT systems are widely used for Java programs
.NET languages are implemented with a JIT system
In essence, JIT systems are delayed compilers

## Slide 44: Preprocessors
Preprocessor macros (instructions) are commonly used to specify that code from another file is to be included
A preprocessor processes a program immediately before the program is compiled to expand embedded preprocessor macros
A well-known example: C preprocessor
  expands #include, #define, and similar macros

## Slide 45: Programming Environments
A collection of tools used in software development
UNIX
  An older operating system and tool collection
  Nowadays often used through a GUI (e.g., CDE, KDE, or GNOME) that runs on top of UNIX
Microsoft Visual Studio.NET
  A large, complex visual environment
Used to build Web applications and non-Web applications in any .NET language
NetBeans
  Related to Visual Studio .NET, except for applications in Java

## Slide 46: Summary
The study of programming languages is valuable for a number of reasons:
  Increase our capacity to use different constructs
  Enable us to choose languages more intelligently
  Makes learning new languages easier
Most important criteria for evaluating programming languages include:
  Readability, writability, reliability, cost
Major influences on language design have been machine architecture and software development methodologies
The major methods of implementing programming languages are: compilation, pure interpretation, and hybrid implementation